## Slide 1: PD Value Guide
VCSEL Driver : DW9854
ToF sensor : 63D
Camera Innovation Group, 2022.11.29

## Slide 2: 전체 Flow
Set 1st current
Read PD_value1[9:0]
Set 2nd current
Read PD_value2[9:0]
1st current : 0xE1 (=2700mA)
2nd current : 0x7D (=1500mA)
Write PD_value2[9:0]
to EEPROM
Write PD_value1[9:0]
to EEPROM
PD 값을 취득하고 EEPROM에 write 하는 과정은 오른쪽 그림과 같다.
자세한 내용은 다음 장에서 설명한다.

## Slide 3: VCSEL Current Setting Method
VCSEL current를 변경하기 위해서는 아래와 같이 I2C 명령어를 동작시킨다.
  write to 0x10 ack data: 0x60 0x28 0x20 0x00 //page setup
  write to 0x10 ack data: 0x60 0x2A 0xE3 0xA0 //start address
  write to 0x10 ack data: 0x6F 0x12 0x00 0x01 //number of write bytes
  write to 0x10 ack data: 0x60 0x28 0x20 0x00 //page setup
  write to 0x10 ack data: 0x60 0x2A 0xE3 0xA2 //address
  write to 0x10 ack data: 0x6F 0x12 0x00 0x08 //register address of VCSEL Driver
  write to 0x10 ack data: 0x60 0x28 0x20 0x00 //page setup
  write to 0x10 ack data: 0x60 0x2A 0xE3 0xA4 //address
  write to 0x10 ack data: 0x6F 0x12 0x00 0xE1 //data for 0x08 (0xE1 is 2700mA)  change this value
  write to 0x10 ack data: 0x60 0x28 0x20 0x00 //page setup
  write to 0x10 ack data: 0x60 0x2A 0xE3 0xA6 //address
  write to 0x10 ack data: 0x6F 0x12 0x00 0xFF //Delay command
  write to 0x10 ack data: 0x60 0x28 0x20 0x00 //page setup
  write to 0x10 ack data: 0x60 0x2A 0xE3 0xA8 //address
  write to 0x10 ack data: 0x6F 0x12 0x00 0x0F //Data for Delay, 13.3us
  write to 0x10 ack data: 0x60 0x28 0x20 0x00 //page setup
  write to 0x10 ack data: 0x60 0x2A 0xE3 0xAA //address
  write to 0x10 ack data: 0x6F 0x12 0x00 0x00 //Terminates command array
  write to 0x10 ack data: 0x60 0x28 0x20 0x00 //page setup
  write to 0x10 ack data: 0x60 0x2A 0xE3 0xE0 //end address
  write to 0x10 ack data: 0x6F 0x12 0x00 0x01 //data at end address
1st Current : 0xE1 (225*12=2700mA)
2nd current : 0x7D (125*12=1500mA)

## Slide 4: PD value Read Method
PD value를 읽기 아래와 같이 I2C 명령어를 동작시킨다.
  write to 0x10 ack data: 0x60 0x28 0x20 0x00
  write to 0x10 ack data: 0x60 0x2A 0xE4 0x0A
  write to 0x10 ack data: 0x6F 0x12 0x00 0x01 //read operation_per_frame
  write to 0x10 ack data: 0x60 0x28 0x20 0x00
  write to 0x10 ack data: 0x60 0x2A 0xE3 0xE2
  write to 0x10 ack data: 0x6F 0x12 0x00 0x23 //address of CHECK_APC_IMOD[9:8]  change this value
  write to 0x10 ack data: 0x60 0x28 0x20 0x00
  write to 0x10 ack data: 0x60 0x2A 0xE3 0xE4
  write to 0x10 ack data: 0x6F 0x12 0xFF 0xFF //termination code
  write to 0x10 ack data: 0x60 0x28 0x20 0x00
  write to 0x10 ack data: 0x60 0x2A 0xE4 0x0E
  write to 0x10 ack data: 0x6F 0x12 0x00 0x01
  write to 0x10 ack data: 0x60 0x2C 0x20 0x00
  write to 0x10 ack data: 0x60 0x2E 0xE3 0xF6 //address of incoming buffer
  read to 0x10 ack data: 0x6F 0x12 0x00 0x00 //Read two bytes. (Return value, Use 2nd value)
Address of CHECK_APC_IMOD[9:8] : 0x23
Address of CHECK_APC_IMOD[7:0] : 0x26

## Slide 5: PD value Write Method
EEPROM에는 아래 영역에 취득한 PD value을 적는다.
조건
  거리: 500mm
  Setfile:
    F1: 100M setfile 사용
    F2: 20M setfile 사용
  EEPROM:
    Fix1: 2700mA 조건에서 취득한 PD value
    Fix2: 1500mA 조건에서 취득한 PD value
Setfile | Current 셋팅 조건
100M setfile 사용 | 2700mA 조건에서 취득
100M setfile 사용 | 1500mA 조건에서 취득
20M setfile 사용 | 2700mA 조건에서 취득
20M setfile 사용 | 1500mA 조건에서 취득